## Slide 1: Dark data: The use of sensor data in process monitoring and control
LCCC Process Control Workshop
September 28-30, 2016
Margret Bauer
School of Electrical and Information Engineering
University of the Witwatersrand
South Africa

## Slide 2: Wits
One of the oldest Universities in South Africa, founded in 1896
Rooted in the mining industry
Most famous student: Nelson Mandela
Famous control engineers: David Limebeer (Oxford), David Mayne (Imperial College), Anthony Bloch (University of Michigan)

## Slide 3
Dark Data
Information assets organizations collect, process and store during regular business activities, but generally fail to use for other purposes.
http://www.gartner.com/it-glossary/dark-data/
Dark Matter
Unidentified type of matter that has not been observed yet, and does not give of or reflect light.
What is Dark Data?
100101010100001011110101010101010101010010101
010101101110101010010101010100101010111110101
100000111110101101011110101011010111010011101
101010101010101010101011101010101010101100010

## Slide 4: Some sources that generate data in an industrial process
Process
measurements
Temperature
Flow
Pressure
Level
Analyzers
(e.g. pH)
Switches
Condition
monitor
Electrical measurements
Valve position
Video
cameras
FC
Control data: Output, setpoint
MPC trajectory
Alarm limits (L, LL, H, HH)
PLC and DCS status: Overload, hard disk, speed

## Slide 5: What happens to the process measurement data?
Field device
Display only
50%
Connected to DCS
50%

## Slide 6: What happens to the process measurement data?
Field device
Display only
50%
Connected to DCS
50%

## Slide 7: What happens to the process measurement data?
Field device
Display only
50%
Connected to DCS
50%

## Slide 8: What happens to the process measurement data?
Field device
Display only
50%
Connected to DCS
Data base
i.e. process historian/
Operational historian
50%

## Slide 9: What happens to the process measurement data?
Field device
Display only
50%
Connected to DCS
Data base
i.e. process historian/
Operational historian
50%

## Slide 10: Is this Big Data?
Wikipedia: Big data is a term for data sets that are so large or complex that traditional data processing applications are inadequate. Volume, Variety, Velocity, Veracity (Uncertainty)
“Before the term Big Data was being used as part of the Internet of Things, plant historians were handling large volumes of time-synchronized data.”
B. Lydon, ISA InTech Magazine Jan/Feb 2015 https://www.isa.org/intech/20150201/

## Slide 11: How to get value out of dark data: Big data analytics
http://www.mckinsey.com/business-functions/operations/our-insights/how-big-data-can-improve-manufacturing
Artificial neural networks
Correlation analysis
Data visualization
Significance testing

## Slide 12: How to get value out of dark data: Big data analytics
http://www.mckinsey.com/business-functions/operations/our-insights/how-big-data-can-improve-manufacturing
Artificial neural networks
Correlation analysis
Data visualization
Significance testing

## Slide 13: How to get value out of dark data
Providing context for the
DATA
Providing context for the
PROBLEM
Notes: Following from this, it is clear that we first of all need to look at the question. I will refer to this as the context for the problem. There is a second aspect which assists in getting value out of dark data and this is to provide context for the data. In the following slides I will elaborate on both propositions.

## Slide 14: Providing context for DATA
P&ID
Maintenance information

## Slide 15: Providing context for DATA
P&ID
Maintenance information
Expert knowledge
95
5.1

## Slide 16: Context of PROBLEM: Objectives of plant operation
Safety
Safety
Safety
Efficiency
Efficiency
Efficiency

## Slide 17: Some problems we can solve with ‘Dark Data’ today
FC
Controller tuning
Control performance monitoring (CPM)
Root cause analysis
Plant asset management
Alarm management
Energy management
Sensor validation
Process modeling
Batch process monitoring

## Slide 18: Control loop performance monitoring: What can we find in the dark data?
Bauer, M., Horch, A., Xie, L., Jelali, M. and Thornhill, N., 2016. The current state of control loop performance monitoring–A survey of application in industry. Journal of Process Control, 38, pp.1-10.
Process variable
Controller output
Saturation
Oscillation
Manual control
Sluggish
Nonlinear
Quantization

## Slide 19: Plant-wide root cause analysis
Bauer, M., Cox, J.W., Caveness, M.H., Downs, J.J. and Thornhill, N.F., 2007. Finding the direction of disturbance propagation in a chemical process using transfer entropy. IEEE transactions on control systems technology, 15(1), pp.12-21.

## Slide 20: Control loop performance monitoring at ABB
Alf Isaksson
ABB
Alexander Horch
PhD, ABB
Nina Thornhill, Secondment at ABB
ABB/RAE Research Chair since 2007
Margret Bauer
PhD, ABB
Kevin
Starr
Patric Boo
OptimizeIT
Loop Performance Manager
Nunzio
Bonavita
CPM on DCS 800xA
Horch, A., Cox, J. W., & Bonavita, N. (2007). Peak performance- root cause analysis of plant-wide disturbances. ABB Review, (1), 24-29.
Starr, K. (2012). Expert access – anytime, anywhere. ABB Review (2), 12-17.
Boo, P. (2015). A service tool grows up. ABB Review (1), 27-31.
2015
2000
2005
2010
2015
Service Port

## Slide 21: ABB’s Service Port – what’s new
Starr, K. D., Petersen, H., & Bauer, M. (2016). Control loop performance monitoring–ABB’s experience over two decades. IFAC-PapersOnLine, 49(7), 526-532.
On site PC and off-site notifications
Considers workflow, i.e.
  Initialization
  Training
  Target setting
  View, Scan, Track
KPI representation
 5,000+ installations
It’s not the algorithm…

## Slide 22: Industrie 4.0: Changing requirements for control engineering
Graphic based on Kunschert & Glaser, VHS4Business Thementag Industrie 4.0, 2015
Industrie 2.0
1870: Mass production, electricity
Industrie 3.0
1969: Computer & automation
Industrie 4.0
2010: Internet of Things, Cyber Phyiscal Systems
Mechanical
Electrical
Pneumatic control
Digital control
IT
Mechanical
Electrical
Mechatronics
IT
Mechanical
Electrical
?

## Slide 23
Bauer, M., Schmidt, W., Schlake, J., Larsen, P. and Johansson, C., 2016. Integrating IT and OT. Leveraging operational technology integration with Decathlon Services. ABB Review (2), 60-67.
ABB’s DECATHLON SERVICES
Contact: Christian Johansson, christian.johansson@se.abb.com (ABB Malmö)

## Slide 24
No (big, dark) data analysis without
Context for DATA and
Context of the PROBLEM
Consider the workflow when developing solutions
Control engineering is moving towards IT
Thanks to: Kevin Brooks, Alexander Horch, Christian Johansson