## Slide 1: On PWC for chemical plants
Krister Forsman
2016-09-29

## Slide 2: Outline
Short facts about specialty chemicals industry and Perstorp
Plantwide control:
  Degrees of freedom
  Throughput manipulator selection
Specifying control objectives

## Slide 3: Characteristics of chemical plants
(A view slightly biased by Perstorp experience)

## Slide 4: Control: What differs between different industries?
For mature processes, with a large installed base, there are standard solutions; often quite advanced. Often packaged by control system suppliers.
  Oil refineries (~800 world wide)
  Paper machines (2000)
For specialized processes, that are fairly unique, local expertise has to design the controls.
  Only a handful of plants in the whole world
  Often confidential processes

## Slide 5: Characteristics of typical specialty chemicals plants
Synthesis (reaction) followed by a large number of separation steps.
Reaction is often batch-wise, and separation continuous.
Separation can be a number of sequential distillations, evaporations, crystallizations, filtrations, centrifuges, decanters, etc.
High value side streams (byproducts); many recycle loops
  The separation part of the plant is much more complex than the synthesis.
  Complex topologies
  Many internal buffers
Plants operate 24/7
Controlled by computerized control systems
Products are liquid, solid or gas

## Slide 6: Topology for plant with multiple separations
Reaction
Separation
Raw material 1
Raw material 2
Raw material 3
Separation
Product 1
Main product
Product 2
Separation
Product 3
Separation
Waste
Waste
(Loosely based on a true story)
Bagging
Bagging

## Slide 7: In reality, much more complicated
How many throughput manipulators?
What is the production rate?
What does ”shutdown” mean ?

## Slide 8: The Perstorp group – short facts
Specialty chemicals company with focus on organic chemistry
  Turnover 2015: ~1200 MEUR
  Profit 2015: ~180 MEUR
  Main owner: PAI Partners, a French equity company
  1500 employees
Products: Mainly additives for other chemical industries
  Additives in paints and coatings, plastic-processing and automotive industries
  Thermoplastics, plasticizers, solvents, bleaching agents, etc
but also end products like feed additives and bio-diesel.
Global Technology has a group of 4-5 people working full time on proces control and industrial IT.

## Slide 9: Nine production sites
Totally ca 40 plants ~50 000 variables ~5 000 control loops
Bruchhausen
Castellanza
Gent
Stenungsund
Perstorp
Toledo
Warrington
Waspik
Zibo

## Slide 10
Degrees of freedom

## Slide 11
Catalytic incineration of VOC
5 manipulated variables
11 process variables
What to control? How?
Reactor
Electric heater
Atm.
Atmosphere
TT
01
TT
16
TT
04
TT
13
TT
11
FT
14
Waste gases from
reactor, distillation, evaporation, vacuum system etc
Heat exchanger
TT
03
Variable speed fan
TT
12
TT
05
TT
02
PT
15

## Slide 12: DoF central concept in PWC
Control engineering point of veiw: Number of independent manipulated variables
  Typically: number of valves. Causality important.
Chemical engineering point of view: Number of independent variables in steady state
The number of controlled variables = number of DoF
Differ between dynamic and static DoF
  Inventories have to be controlled. Each one consumes a dynamic DoF.
  The remaining ones quantify the static behavior of the process.
Most expositions lack a rigorous mathematical definition.
  This should be possible using algebraic concepts, such as transcendence degree of extension fields.

## Slide 13: Different competencies for different levels in the structure
Closing a loop does not reduce the #DoF. We have to choose setpoint.
Moving DOFs upwards in the hierarchy requires several competencies.
Valve
FC
LC
PI-controller
Cascade control
LC.SP
Buffert optimization
Control engineer
Control engineer
Process engineer
Example 1
Valve
TC
TC.SP
PI-controller
Crystallization theory
Control engineer
Process engineer
Example 2

## Slide 14
Aspects of
Plant wide control
The throughput
manipulator

## Slide 15: Throughput manipulator determines production rate
A plant always has a variable that determines the troughput rate:
  It is normally a flow, the “master flow”. The “gas pedal”
  Called TPM = throughput manipulator
  If you have very large buffers between process areas, where level is not controlled, you may in fact have several TPMs.
The operator gives the setpoint for the TPM.
All other flows are given indirectly by the master flow, typically through level controls.
You have to select a variable that is TPM: the choice is either deliberate or inadvertent.

## Slide 16: Choice of TPM: Bottle neck or minimum variation
The two most common ways of selecting which variable is TPM:
  The flow closest to the bottle neck.
  The flow most important to keep constant.
Reason: The TPM flow will be the “most constant” one.
If no thought is given to the choice, then often the first flow in the plant becomes TPM.

## Slide 17: Unconsidered choice of TPM gives suboptimal operation
Example: In a plant the feed of reactant 1 was chosen as TPM.
The filtration step is the bottle neck.
Which variable should be master flow in order to give maximum production with minimum number of SP changes?
Reactor
Post
reaction
Filtration
Storage
FC3
FC1
FC2
Operator SP
FC4
FC5
Reactant 1
Reactant 2

## Slide 18: Solution: Filter feed = TPM
The setpoint for the filter feed flow is set by operator / plant manager.
Other flows are a consequence of level controls or similar.
Reactor
Post
reaction
Filtration
Storage
FC3
FC1
FC2
FC4
FC5
Reactant 1
Reactant 2
Operator SP

## Slide 19: Inventory controls; real example
3
4
FC4
TPM
2
FC5
FC3
FC2
1
FC1
Four tanks in series. One thruput manipulator (TPM). Level controllers.
The ”radiating rule” gives the control topology below.

## Slide 20: Radiating rule is not mandatory
3
4
FC4
TPM
2
FC5
FC3
FC2
1
FC1
The topology below will also work.
  Easy to realize that the entire process can be stabilized using only PI controllers.
Disadvantage: LC2 won’t work if LC1 is in manual.
However, it has an advantage too...

## Slide 21: FC1 sometimes fixed
3
4
FC4
TPM
2
FC5
FC3
FC2
1
FC1
TPM
3
4
FC4
TPM
2
FC5
FC3
FC2
1
FC1
TPM
At times, the operator needs to run flow 1 with fixed SP.
Since tank 1 is much smaller than tank 2, it is easier to handle the process if level 1 is still controlled automatically, and FC1 is used to manually control level 2.

## Slide 22: This can be made to work too...
TPM
...meaning all levels can be stabilized using only PI-controllers.

## Slide 23: Even this ”works”
TPM
LC1
LC2
FC2
FC1
But not if both LCs are PI-ctrl. One has to be a PID.
Maybe this can be made into a general indicator?
  If you can’t stabilize the plant without resorting to using derivative action, the structure is not ”good”.

## Slide 24: TPM selection and consistency
FC
FC
FC
FC
FC
FC
FC
How many of the flows can be set independently?
Which combinations of flows?

## Slide 25: This works
q2
q1
FC
FC
FC
FC
FC
FC
FC
TPM
LC
LC
LC
LC
q0

## Slide 26: This is inconsistent
FC
FC
FC
FC
FC
FC
FC
TPM
TPM
TPM

## Slide 27: This is also inconsistent
FC
FC
FC
FC
FC
FC
FC
TPM
TPM
TPM

## Slide 28: Algorithm for finding all consistent schemes
1
3
2
4
q1
q2
q3
q4
q5
q6
q7

## Slide 29: Most plants have several TPMs
This is possible because there are intermediate buffers inside the plant.
An indicator of this is that there is a large number of setpoint changes for some of the flows.
  Visible e.g. in operator action statistics.
Why not have a completely automated plant where buffer levels are controlled automatically (by P-controllers)?
  ”Bullwhip” effect
  Difficult to foresee all possible scenarios

## Slide 30: An overlooked issue in TPM selection
The choice of TPM affects the precision in production planning:
  If the TPM is located far away from the point where production is measured, it becomes more difficult to adhere to the production plan.
  Plant management / operator has to guess what “speed” to choose in order to produce the right number of tons.
Tons produced
TPM setpoint

## Slide 31: PWC issues should be included in control projects
The plant-wide control strategy is a very important tool for making a plant operate efficiently.
  Degrees-of-freedom analysis for enumerating all possible PWC schemes
  Thruput manipulator selection
Unfortunately PWC is often not taught in courses.
  Somehow falls between chemical engineering and control theory.
Process engineers rarely use a systematic approach to choose PWC strategy.
But ”PWC thinking” should be a part of all investment projects and control projects.

## Slide 32
Control
specifications

## Slide 33: Specifying control objectives
Examples of control specifications are
  Keep the PV as close as possible to the setpoint when there are disturbances, while not moving the MV too much.
  The controller should be possible to run in Auto during startups.
  Minimize outlet flow variations while keeping the level within some limits.
  Maximize reactor throughput while keeping temperature within limits.
It is often hard to obtain a scientific description of the control objectives.
  There may be implicit requirements.
Control engineers don’t always have a deep understanding of the process.
Process engineers are normally not used to specifying control objectives.
  What are constraints and what is target function?

## Slide 34: Example: Split flow
FT
FC1
FT2
FT3
Stream 1
Stream 2
Liquid (incompressible) flow. The total flow is controlled by FC1.
  Introduce a way to split the flow between stream 1 and stream 2.
  Of course, controlling both flow 2 and flow 3 is impossible.

## Slide 35: Simple solution: ratio control
FT
FC1
FT2
FC3
FT3
x
Ratio entered
by operator
FV2
FV3
Traditional ratio control (below) lets the operator specify flow 3 as a factor of flow 2. FV2 is fixed (but not closed).
  This solution was not accepted by operational staff.
  They sometimes have to set flow 2 as a factor of flow 3.
  Total pressure drop should be as small as possible
Which structure can we use now?

## Slide 36: This solves the split control problem
FT3
FT2
FC4
+
Desired
split
0-1
PV
SP
OP
FT
FC1
FV2
FV3
x
Desired split FT2/Total is entered by the operator

## Slide 37: Some things should be left to the operators
Complex control solutions make it hard for the operator to know which situations are handled automatically.
Sometimes the control solution does not cover all the scenarios that the operator has to handle.
  Some requirements were forgotten in the specifications.
More automation may increase the cognitive load on the operator.
Compare: Adaptive cruise control

## Slide 38
Thank you!